Robust, Simple Page Segmentation using Hybrid Convolutional MDLSTM Networks
Thomas Breuel
NVIDIA Research

---
Single Step Deep Learning Layout Analysis
Single Step Deep Learning Layout Analysis
- simple deep learning approach
- convolutional layers + MDLSTM layers
- trainable, adapts to document databases
- simultaneously performs: text/image segmentation, border noise removal, text/math segmentation, text line detection
- robust to noise
- can be applied directly to grayscale, photographic images
- runs on GPU (1 sec / page)
- comparable performance to existing layout analysis systems using just 1600 training pages

---
Deep Learning Architecture for Layout Analysis
Deep Learning Architecture for Layout Analysis

---
Single Step Border Removal, Multicolumn Textline Finding
Single Step Border Removal, Multicolumn Textline Finding

---
Single Step Border Removal, Math Removal, Figure Removal, Text Line Detection

---
Direct Application to Grayscale Input
Direct Application to Grayscale Input

---
Deep Segmenter vs Tab Segmenter
Deep Segmenter vs Tab Segmenter
The Deep Segmenter performs comparable to, or slightly better than, the Tab Segmenter.
Results on page frame only (border noise removed).

---
Ground Truth Prep vs Layout Analysis Training
Ground Truth Prep vs Layout Analysis Training

---
Training for Different Detection Tasks
Training for Different Detection Tasks
original page
body text detection
text detection
text frame detection
border noise detection

---
Line Extraction from Text Center Lines
Line Extraction from Text Center Lines
The text center lines identified by the DNN are used as seeds for identifying the connected components belonging to the actual text line.
Each connected component within a halo around the text center line seed is assigned to the closest seed.

---
Layout Analysis with Deep Learning
Layout Analysis with Deep Learning
Deep Neural Network computes text line centers from binary or grayscale document image. Images, math, etc. are implicitly removed.
For each identified text line center, all the closest connected components within a halo are assigned to the line.